## Slide 1: OnScreen Programming
By Ben Shepard

## Slide 2: Contents
What is it?
Firmware
Instructions
Buttons
  Goto
  Delay
  Output
Sample Program

## Slide 3: What is it?
Onscreen programming for legomindstorms is a firmware that lets you program the RCX without the use of a computer. You simply use the Program and View buttons to make up your program.
The onscreen programming program is given to you as a firmware which you download to your RCX using the infra red tower given to you when you purchase the Robotics invention system.
It works on the hex (base 16) system. 1,2,3,4,5,6,7,8,9,a,b,c,d,e,f.

## Slide 4: Firmware
To get the firmware into your RCX, I suggest using the SDK Software
Get it from the Tips & Tricks section on the legomindstorms site
Put the firmware in the SDK directory and type in the new firmware box “onscreen.sre”
Then click on the the New firmware button

## Slide 5: Instructions
Press the On/Off button on your RCX
A screen should come up with the word Lego
Press the Run button once to take you to the programming screen
You will notice there is a flashing cursor underneath one of the numbers

## Slide 6: Instructions
The Screen is arranged in this way:
SS 12 C A B C
SS = Step
12 = Argument (s)
C = Command (Delay, Output, Goto)

## Slide 7: Buttons
You will notice a flashing cursor underneath the numbers
The View button moves the cursor
The Program button changes the selection above the cursor
The Run button starts and stops the current program

## Slide 8: Buttons
When the cursor is under SS (step), pressing Program advances to the next step. The numbers show what step you are editing

## Slide 9: Buttons
When the cursor is under C (command), pressing Program changes the command There are three commands:
G = Goto
D = Delay
O = Output

## Slide 10: Goto
Use the goto command to go to another command
Select the goto command and change the argument to the command number you want to go to

## Slide 11: Delay
Use the Delay command to make the RCX pause for the programmed amount of time
It is used after an output or goto command
Select the delay command and change the argument to the time wanted to wait
10 = 1 second

## Slide 12: Output
Use the output command to turn on or off motors
Select the output command and use the command to change which motors go on
Use the view button and move them to the arrows where you can change the direction of the motors
To turn all motors off, go to the argument section and press Program until it displays “–”

## Slide 13: Sample Program
00.14 d Wait 2 seconds
01. 8 o > > > Backwards all motors Power 8
02.14 d Wait 14 seconds
03. - o > > > Stop all motors
04.14 d Wait 2 seconds
05. 8 o < < < Forwards all motors Power 8
06.14 d Wait 2 seconds

## Slide 14: Sample Program
07. - o < < < Stop all motors
08.14 d Wait 2 seconds
09.00 g Go to step 00
This program will make a robot with tracks go backwards and forwards